## Slide 1: The ARM Cortex-M4 Processor Architecture
Notes: Before programming an application for an unknown processor, it is essential to get familiar with it. We can do this by discovering and analysing the architecture of the chip and the way components are communicating with each other. We will also learn about interrupt/threading/tasking methods, internal registers, low level command sets, and much more.
Learning a new processor family usually begins with its architecture. Every single processor type has its own, but there are similarities among processor families and subfamilies. One family is the ARM Cortex M, in particular the M4 subseries.

## Slide 2: Learning Objectives
At the end of this lecture, you should be able to:
Outline the features and benefits of the Arm Cortex-M4 processor.
Outline the functions of the Cortex-M4 processor components including Nested Vectored Interrupt Controller (NVIC), Wakeup Interrupt Controller (WIC), Memory Protection Unit (MPU), Bus Interconnect and Debug System.
Describe the Cortex-M4 processor core registers including their functions.

## Slide 3: Module syllabus
ARM Architectures and Processors
  What is ARM Architecture
  ARM Processor Families
  ARM Cortex-M Series
  Cortex-M4 Processor
  ARM Processor vs. ARM Architectures
ARM Cortex-M4 Processor
  Cortex-M4 Processor Overview
  Cortex-M4 Block Diagram
  Cortex-M4 Registers
Notes: In this module, the ARM architecture will be comprehensively classified among the ARM processor families, and will be analyzed. Because ARM is not a chip-manufacturer, ARM-based cores are used by numerous companies for their controllers. This makes ARM architectures a broadly accepted industry standard.
Following an overview of the general ARM architecture, and a brief overview of the processor families, this module focus on the M4 processor subfamily. The M4 subfamily is the most comprehensive group of mobile (M-type) processors.
Note that, because in this course provides only an overview with few examples, it will be necessary for more extensive projects to use the dedicated processor manuals (shown on the last slide of this module), which describe all functions in more detail.

## Slide 4: ARM architectures and processors
ARM architecture is a family of RISC-based processor architectures
  Well-known for its power efficiency
  Hence widely used in mobile devices, e.g., smartphones and tablets
  Designed and licensed by ARM to a wide eco-system of partners
ARM Holdings
  The company that designs ARM-based processors
  ARM does not manufacture, but it licenses designs to semiconductor partners who add their own Intellectual Property (IP) on top of ARM’s IP, which they then fabricate and sell to customers.
  ARM also offers IP other than processors, such as physical IPs, interconnect IPs, graphics cores and development tools.
Notes: Although ARM processors are widely considered as something like an industry standard, ARM itself does not produce any controllers. Instead, ARM designs the processor cores of controllers in its hardware libraries, and licenses them to producers. The producers combine this IP with their own IP, or other third party IP, to create a complete product. A wide eco-system of development tools and manuals are provided.

## Slide 5: ARM processor families
Cortex-A series (Application)
  High performance processors capable of full Operating System (OS) support
  Applications include smartphones, digital TV, smart books
  Cortex-R series (Real-time)
  High performance and reliability for real-time applications;
  Applications include automotive braking system, powertrains
  Cortex-M series (Microcontroller)
  Cost-sensitive solutions for deterministic microcontroller applications
  Applications include microcontrollers, smart sensors
  SecurCore series for high security applications
Earlier classic processors including ARM7, ARM9, ARM11 families
Cortex-A
Cortex-A73 Cortex-A72 Cortex-A57 Cortex-A53 Cortex-A35 Cortex-A32
Cortex-R
Cortex-M
SecurCore
Classic
Cortex-A17 Cortex-A15 Cortex-A9 Cortex-A8 Cortex-A7 Cortex-A5
Cortex-R8 Cortex-R7 Cortex-R5 Cortex-R4
Cortex-M7, Cortex-M23, Cortex-M33 Cortex-M4 Cortex-M3 Cortex-M0+ Cortex-M0
SC000
SC300
ARM11
ARM9
ARM7
Notes: ARM’s processor families range from the A-series, which are optimized for rich operating systems, the R-series, which are optimized for hard real-time applications and high performance, the M-series, which is optimized for discrete processing and microcontroller, and the SecurCore, which is optimized for security applications.
ARM Cortex-A processors are at the heart of the most powerful and compelling technology products. They are deployed in mobile devices, networking infrastructure, home and consumer devices, automotive in-vehicle infotainment and driver automation systems, and embedded designs.
ARM Cortex-R real-time processors offer high-performance computing solutions for embedded systems where reliability, high availability, fault tolerance and/or deterministic real-time responses are needed. Cortex-R processors are used in products that must always meet exacting performance requirements and timing deadlines.
The ARM Cortex-M processor family is a range of scalable, energy efficient, and easy to use processors that meet the needs of tomorrow’s smart and connected embedded applications. The processors are supported by the world’s number one embedded ecosystem, and have already been shipped in many billions of devices.
The ARM SecurCore processor family provides powerful 32-bit secure solutions based upon industry leading ARM architecture. By enhancing highly successful ARM processors with security features, SecurCore gives smart card and secure IC developers easy access to the benefits of ARM 32-bit technology such as small die size, energy efficiency, low cost, excellent code density and outstanding performance.
ARM Classic processors include the ARM11, ARM9 and ARM7 processor families. These processors are still widely licensed around the globe, providing cost-effective solutions for many of today's applications.

## Slide 6: How to design an ARM-based SoC
Select a set of IP cores from ARM and/or other third-party IP vendors
Integrate IP cores into a single chip design
Give design to semiconductor foundries for chip fabrication
ARM-based
SoC
ROM
ARM
processor
RAM
System bus
Peripherals
External Interface
SoC
SoC Design
Chip Manufacture
Licensable IPs
IP libraries
Cortex-A9
Cortex-R5
Cortex-M4
ARM7
ARM9
ARM11
AXI bus
AHB bus
APB bus
GPIO
I/O blocks
Timer
DRAM ctrl
FLASH ctrl
SRAM ctrl
Notes: An ARM-based SoC is designed by selecting elements from ARM IP libraries and/or other third party IP vendors. Different components such as core, RAM, ROM, peripherals, etc. are selected from licensable IP. These IP components are combined with company-owned or additional third-party IP to create a system-on-a-chip (SoC). Finally, this “virtual” know-how is brought to silicon in a semiconductor foundry for ARM-based SoC fabrication.

## Slide 7: ARM Cortex-M series
Cortex-M series: Cortex-M0, M0+, M3, M4, M7, M23, M33, M55
Energy-efficiency
  Lower energy cost, longer battery life
Smaller code
  Lower silicon costs
Ease of use
  Faster software development and reuse
Embedded applications
  Smart metering, human interface devices, automotive and industrial control systems, white goods, consumer products and medical instrumentation
Notes: This course is about M-series-processors, optimized for low energy consumption and small codes, requiring less physical space and silicon for lower cost. These cores are optimized for mobile applications with independent power supply.
ARM offers Cortex-M0 and Cortex M0+ for applications requiring minimal cost, power, and area while Cortex-M3 and Cortex-M4 and Cortex-M7 are designed for applications requiring higher performance. ARM Cortex-M4 and Cortex-M7 integrate Digital Signal Processing (DSP) and accelerated floating point processing capability for fast and power-efficient algorithm processing of digital signal control applications.

## Slide 8: ARM processors vs. ARM architectures
ARM architecture
  Describes the details of instruction set, programmer’s model, exception model, and memory map
  Documented in the Architecture Reference Manual
ARM processor
  Developed using one of the ARM architectures
  More implementation details, such as timing information
  Documented in processor’s Technical Reference Manual
ARMv4/v4T Architecture
ARMv5/ v4E Architecture
ARMv6 Architecture
ARMv7
Architecture
ARM v6-M
e.g. Cortex-M0, M1
e.g. ARM7TDMI
e.g. ARM9926EJ-S
e.g. ARM1136
ARMv8 Architecture
ARMv7-A
e.g. Cortex-A9
ARMv7-R
e.g. Cortex-R4
ARMv7-M
e.g. Cortex-M4
ARMv8-A
e.g. Cortex-A53
Cortex-A57
ARMv8-R
ARMv8-M
Notes: While programming ARM systems, a distinction needs to be made between the ARM architecture and an ARM processor. ARM architecture describes the details related to programming including data types, instructions, registers, memory architecture etc. Companies that are licensing ARM architecture are using their own CPU design.
ARM architecture forms the basis for every ARM processor. Over time, the ARM architecture has evolved to include architectural features that meet the growing demand for new functionality, integrated security features, high performance and the needs of new and emerging markets. There are currently three ARMv8 profiles: (1) the ARMv8-A architecture profile for high performance markets such as mobile and enterprise, (2) the ARMv8-R architecture profile for embedded applications in automotive and industrial control, and (3) the ARMv8-M architecture profile for embedded and IoT applications.
The ARM architecture supports implementations across a wide range of performance points, establishing it as the leading architecture in many market segments. The ARM architecture supports a very broad range of performance points, leading to very small implementations of ARM processors, and very efficient implementations of advanced designs using state of the art micro-architecture techniques. Implementation size, performance, and low power consumption are key attributes of the ARM architecture.

## Slide 9: ARM Cortex-M series family
Processor | ARM Architecture | Core Architecture | Thumb® | Thumb®-2 | Hardware Multiply | Hardware Divide | Saturated Math | DSP Extensions | Floating Point
Cortex-M0 | ARMv6-M | Von Neumann | Most | Subset | 1 or 32 cycle | No | No | No | No
Cortex-M0+ | ARMv6-M | Von Neumann | Most | Subset | 1 or 32 cycle | No | No | No | No
Cortex-M3 | ARMv7-M | Harvard | Entire | Entire | 1 cycle | Yes | Yes | No | No
Cortex-M4 | ARMv7E-M | Harvard | Entire | Entire | 1 cycle | Yes | Yes | Yes | Optional
Cortex-M7 | ARMv7E-M | Harvard | Entire | Entire | 1 cycle | Yes | Yes | Yes | Optional
Notes: This table provides a good overview of the features of each single core in the M series family.
Note that the Cortex M0 andM0+ are optimized for simple sensing and controlling, whereas the M3,M4 and M7 are optimized for data intense operations with Harvard architecture, dedicated (fast) hardware multipliers, math-packages and extensions for digital signal processors(M4 and M7 only).
Thumb stands for variable length execution sets with a length of 16 or 32 bit.

## Slide 10: Cortex-M4 processor overview
Cortex-M4 Processor
  Introduced in 2010
  Designed with a large variety of highly efficient signal processing features
  Features extended single-cycle multiply accumulate instructions, optimized SIMD arithmetic, saturating arithmetic and an optional Floating Point Unit.
High performance efficiency
  1.25 DMIPS/MHz (Dhrystone Million Instructions Per Second / MHz) at the order of µWatts / MHz
Low power consumption
  Longer battery life – especially critical in mobile products
Enhanced determinism
  The critical tasks and interrupt routines can be served quickly in a known number of cycles
Notes: The ARM Cortex-M4 processor is a high performance embedded processor with DSP instructions, developed to address digital signal control markets that demand an efficient, easy-to-use blend of control and signal processing capabilities. The processor is highly configurable, enabling a wide range of implementations from those requiring floating point operations, memory protection and powerful trace technology, to cost sensitive devices requiring minimal area.

## Slide 11: Cortex-M4 processor features
32-bit Reduced Instruction Set Computing (RISC) processor
Harvard architecture
  Separated data bus and instruction bus
Instruction set
  Includes the entire Thumb®-1 (16-bit) and Thumb®-2 (16/ 32-bit) instruction sets
3-stage + branch speculation pipeline
Performance efficiency
  1.25 – 1.95 DMIPS/MHz (Dhrystone Million Instructions Per Second / MHz)
Supported interrupts
  Non-Maskable Interrupt (NMI) + 1 to 240 physical interrupts
  8 to 256 interrupt priority levels
Notes: The Cortex-M4 processor is built on a high-performance processor core, with a 3-stage pipeline Harvard architecture, making it ideal for demanding embedded applications. The processor delivers exceptional power efficiency through an efficient instruction set and extensively optimized design, providing high-end processing hardware, including optional IEEE754-compliant single-precision floating-point computation, a range of single-cycle and SIMD multiplication and multiply-with-accumulate capabilities, saturating arithmetic and dedicated hardware division.
To facilitate the design of cost-sensitive devices, the Cortex-M4 processor implements tightly-coupled system components that reduce processor area while significantly improving interrupt handling and system debug capabilities. The Cortex-M4 processor implements a version of the Thumb® instruction set based on Thumb-2 technology, ensuring high code density and reduced program memory requirements. The Cortex-M4 instruction set provides the exceptional performance expected of a modern 32-bit architecture, with the high code density of 8-bit and 16-bit microcontrollers.

## Slide 12: Cortex-M4 processor features
Supports sleep modes
  Up to 240 wake-up interrupts
  Integrated WFI (Wait For Interrupt) and WFE (Wait For Event) instructions and sleep on exit capability (to be covered in more detail later)
  Sleep & deep sleep signals
  Optional retention mode with ARM Power Management Kit
Enhanced instructions
  Hardware divide (2-12 Cycles)
  Single-cycle 16, 32-bit MAC, single-cycle dual 16-bit MAC
  8, 16-bit SIMD arithmetic
Notes: Cortex-M4 supports up to 240 wake-up interrupts, and it offers integrated WFI (Wait For Interrupt) and WFE (Wait For Event) instructions and sleep on exit capabilities. The Cortex-M4 processor sleep modes reduce power consumption. The modes can be “sleep mode”, stopping the processor clock, or “deep sleep mode”, stopping the system clock and switching off the PLL and flash memory.
Enhanced instructions are considered as DSP extensions.

## Slide 13: Cortex-M4 processor features
Debug
  Optional JTAG & Serial-Wire Debug (SWD) Ports
  Up to 8 breakpoints and 4 watchpoints
Memory Protection Unit (MPU)
  Optional 8 region MPU with sub regions and background region
Notes: The Cortex-M4 processor can implement a complete hardware debug solution. This provides high system visibility of the processor and memory through either a traditional JTAG port or a 2-pin Serial Wire Debug (SWD) port that is ideal for microcontrollers and other small package devices.
The Memory Protection Unit (MPU) improves system reliability by defining the memory attributes for different memory regions. It provides up to eight different
regions, and an optional predefined background region

## Slide 14: Cortex-M4 processor features
ARM Cortex-M4 Implementation Data |  |  | 
Process | 180ULL (7-track, typical 1.8v, 25C) | 90LP (7-track, typical 1.2v, 25C) | 40G (9-track, typical 0.9v, 25C)
Dynamic Power | 151 µW/MHz | 32.82 µW/MHz | 12.26 µW/MHz
Floorplanned Area | 0.44 mm2 | 0.119 mm2 | 0.028 mm2
The Cortex-M4 processor is designed to meet the challenges of low dynamic power constraints while retaining light footprints
  180ULL ultra low power process –151 µW/MHz
  90LP low power process – 32.82 µW/MHz
  40LP low power process – 12.26 µW/MHz

## Slide 15: Cortex-M4 block diagram
Optional
WIC
Nested Vector
Interrupt
Controller
(NVIC)
Optional
Debug
Access Port
ARM Cortex-M4 Microprocessor
Optional Memory
protection unit
Bus matrix
Code interface
SRAM and
peripheral interface
Optional FPU
Processor core
Optional
Embedded
Trace Macrocell
Optional Serial
Wire Viewer
Optional
Flash
patch
Optional
Data
watchpoints
interrupt
components
real-time
program
tracing
memory interfaces
data
tracing
Notes: The Cortex-M4 processor features a low gate count processor core, with low latency interrupt processing that has a subset of the Thumb instruction set.
CortexM4 optionally offers a Floating Point Unit (FPU). It also provides a Nested Vectored Interrupt Controller (NVIC) closely integrated with the processor core to achieve low latency interrupt processing with optional Wake-up Interrupt Controller (WIC) feature, providing ultra-low power sleep mode support. Cortex-M4 can optionally provide a MPU (Memory Protection Unit) for memory protection. The Bus interfaces comprises of three Advanced High-performance Bus-Lite (AHB-Lite) interfaces and Private Peripheral Bus (PPB).
Low-cost debug solution features debug access to all memory and registers in the system, Serial Wire Debug Port (SW-DP) or Serial Wire JTAG Debug Port (SWJ-DP) debug access, or both. Optionally Cortex-M4 offers Flash Patch and Breakpoint (FPB) unit for implementing breakpoints and code patches, Data Watchpoint and Trace (DWT) unit for implementing watchpoints, data tracing, and system profiling, Instrumentation Trace Macrocell (ITM) for support of printf style debugging, Trace Port Interface Unit (TPIU) for bridging to a Trace Port Analyzer (TPA) and Embedded Trace Macrocell (ETM) for instruction trace.

## Slide 16: Cortex-M4 block diagram
Processor core
  Contains internal registers, the ALU, data path, and some control logic
  Registers include sixteen 32-bit registers for both general and special usage
Processor pipeline stages
  Three-stage pipeline: fetch, decode, and execution
  Some instructions may take multiple cycles to execute, in which case the pipeline will be stalled
  Speculatively prefetches instructions from branch target addresses
  Up to two instructions can be fetched in one transfer (16-bit instructions)
Fetch
Decode
Execute
Fetch
Decode
Execute
Fetch
Decode
Execute
Instruction 1
Instruction 2
Instruction 3
Fetch
Decode
Execute
Instruction 4
Time
Notes: The Cortex-M4 processor is a 3 stage-pipeline (fetch, decode, execute) core with branch speculation, sixteen 32-bit registers and up to two fetched instructions per transfer.
Due to the instruction buffer in the Cortex-M4, the pipeline operations are different from traditional RISC processors. Consequently, up to two instructions can be fetched in one cycle because most instructions are 16-bit, and an instruction can be fetched several cycles ahead of the decode and execution stages.

## Slide 17: Cortex-M4 block diagram
Nested Vectored Interrupt Controller (NVIC)
  Up to 240 interrupt request signals and a Non-Maskable Interrupt (NMI)
  Automatically handles nested interrupts, such as comparing priorities between interrupt requests and the current priority level
Wakeup Interrupt Controller (WIC)
  For low-power applications, the microcontroller can enter sleep mode by shutting down most of the components.
  When an interrupt request is detected, the WIC can inform the power management unit to power up the system.
Memory protection unit (optional)
  Used to protect memory content, e.g., make some memory regions read-only or preventing user applications from accessing privileged application data
Notes: The NVIC supports up to 240 interrupts, each with up to 256 levels of priority that can be changed dynamically. The processor and NVIC can be put into a very low-power sleep mode, leaving the Wake Up Controller (WIC) to identify and prioritize interrupts. Also, the processor supports both level and pulse interrupts.
The MPU is an optional component for memory protection. The processor supports the standard ARMv7 Protected Memory System Architecture model. MPU mismatches and permission violations invoke the programmable-priority MemManage fault handler. MPU can be used to enforce privilege rules, separate processes or enforce access rules.

## Slide 18: Cortex-M4 block diagram
Bus interconnect
  Allows data transfer to take place on different buses simultaneously
  Provides data transfer management, e.g. write buffer, bit-oriented operations (bit-band)
  May include bus bridges (e.g. AHB-to-APB bus bridge) to connect different buses into a network using a single global memory space
  Includes the internal bus system, the data path in the processor core, and the AHB LITE interface unit
Debug subsystem
  Handles debug control, program breakpoints, and data watchpoints
  When a debug event occurs, it can put the processor core in a halted state, so developers can analyse the status of the processor, such as register values and flags, at that point.
Notes: The Cortex-M4 processor contains three external Advanced High-performance Bus (AHB)-Lite bus interfaces and one Advanced Peripheral Bus (APB) interface.
AHB is a subset of the full AMBA AHB protocol specification. It provides all of the basic functions required by the majority of AMBA AHB subordinate and manager designs, particularly when used with a multi-layer AMBA interconnect.
APB is designed for use with ancillary or general-purpose peripherals such as timers, interrupt controllers, UARTs, and I/O ports. Connection to the main system bus is through a system-to-peripheral bus bridge that helps to reduce system power consumption.
The processor implementation determines the debug configuration, including whether debug is implemented. Basic debug functionality includes processor halt, single-step, processor core register access, Vector Catch, unlimited software breakpoints, and full system memory access.

## Slide 19: ARM Cortex-M4 processor registers
Processor registers
  The internal registers are used to store and process temporary data within the processor core
  All registers are inside the processor core, hence they can be accessed quickly
  Load-store architecture
          To process memory data, they have to be first loaded from memory to registers, processed inside the processor core using register data only, and then written back to memory if needed
Cortex-M4 registers
  Register bank
          Sixteen 32-bit registers (thirteen are used for general-purpose)
  Special registers
Notes: The processor has 32-bit registers that includes 13 general-purpose registers and several special-purpose registers. It has 13 general-purpose registers (R0-R12), a Stack Pointer (SP) R13, a Link Register (LR) R14, a Program Counter (PC) R15 and Special-purpose Program Status Registers, (xPSR).

## Slide 20: Cortex-M4 registers
R0
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
R12
R13(banked)
R14
R15
x PSR
Stack Pointer (SP)
Link Register (LR)
Program Counter (PC)
PRIMASK
CONTROL
Program Status Registers (PSR)
Interrupt mask register
Stack definition
Special registers
Register bank
MSP
PSP
Main Stack Pointer
Process Stack Pointer
APSR
EPSR
IPSR
Application
PSR
Execution
PSR
Interrupt
PSR
Low
Registers
High
Registers
General purpose
register
FAULTMASK
BASEPRI

## Slide 21: Cortex-M4 registers
R0 – R12: general purpose registers
  Low registers (R0 – R7) can be accessed by any instruction
  High registers (R8 – R12) sometimes cannot be accessed e.g. by some Thumb (16-bit) instructions
R13: Stack Pointer (SP)
  Records the current address of the stack
  Used for saving the context of a program while switching between tasks
  Cortex-M4 has two SPs: Main SP, used in applications that require privileged access e.g. OS kernel, and Process SP, used in base-level application code (when not running an exception handler)
Data
Data
PC
SP
Address
Low
High
PUSH
POP
Stack
Code
Heap
Notes: The general-purpose registers R0-R12 have no special architecturally-defined uses. Most instructions that can specify a general-purpose register can specify R0-R12.
Low registers:
Registers R0-R7 are accessible by all instructions that specify a general-purpose register.
High registers:
Registers R8-R12 are accessible by all 32-bit instructions that specify a general-purpose register. Registers R8-R12 are not accessible by most 16-bit instructions.
Registers R13, R14, and R15 have the following special functions:
Stack pointer:
Register R13 is used as the Stack Pointer (SP). Because the SP ignores writes to bits [1:0], it is autoaligned to a word, four-byte boundary.
Handler mode always uses SP_main, but you can configure Thread mode to use either SP_main or SP_process.

## Slide 22: Cortex-M4 registers
Program Counter (PC)
  Records the address of the current instruction code
  Automatically incremented by four at each operation (for 32-bit instruction code), except branching operations
  A branching operation, such as function calls, will change the PC to a specific address, while saving the current PC to the Link Register (LR)
Data
Data
PC
SP
Address
Low
High
PUSH
POP
Stack
Code
Heap
Notes: Program counter:
Register R15 is the Program Counter (PC). PC holds the address of the current instruction that is fetched. Bit [0] is always 0, so instructions are always aligned to word or halfword boundaries.

## Slide 23: Cortex-M4 registers
R14: Link Register (LR)
  The LR is used to store the return address of a subroutine or a function call
  The program counter (PC) will load the value from LR after a function is finished
PC
LR
Main
Program
code
subroutine
Current PC
Load PC with the address in LR to return to the main program
Current LR
Return from subroutine to main program
PC
LR
Main
Program
code
subroutine
Current PC
1. Save current
PC to LR
2. Load PC with the starting address of the subroutine
Call a subroutine
Code region
Code region
Notes: The Link register (R14) is the subroutine Link Register (LR). The LR receives the return address from PC when a Branch and Link (BL) or Branch and Link with Exchange (BLX) instruction is executed. The LR is also used for exception return. At all other times, you can treat R14 as a general-purpose register.

## Slide 24: Cortex-M4 registers
xPSR, combined Program Status Register
  Provides information about program execution and ALU flags
    Application PSR (APSR)
    Interrupt PSR (IPSR)
    Execution PSR (EPSR)
N
Z
C
V
ISR number
Reserved
Reserved
ICI/IT
Reserved
T
Reserved
ISR number
APSR
IPSR
EPSR
xPSR
bit0
bit8
bit16
bit24
bit31
Q
ICI/IT
T
N
Z
C
V
Q
ICI/IT
ICI/IT
Notes: The Program Status Register (PSR) combines the Application Program Status Register (APSR), Interrupt Program Status Register (IPSR) and the Execution Program Status Register (EPSR).
These registers are mutually exclusive bitfields in the 32-bit PSR register.

## Slide 25: Cortex-M4 registers
APSR
  N: negative flag – set to one if the result from ALU is negative
  Z: zero flag – set to one if the result from ALU is zero
  C: carry flag – set to one if an unsigned overflow occurs
  V: overflow flag – set to one if a signed overflow occurs
  Q: sticky saturation flag – set to one if saturation has occurred in saturating arithmetic instructions, or overflow has occurred in certain multiply instructions
IPSR
  ISR number – current executing interrupt service routine number
EPSR
  T: Thumb state – always one since Cortex-M4 only supports the Thumb state (more on processor states in the next module)
  IC/IT: Interrupt-Continuable Instruction (ICI) bit, IF-THEN instruction status bit
Notes: The APSR contains the current state of the condition flags from previous instruction executions, whereas IPSR contains the exception type number of the current Interrupt Service Routine (ISR).
The EPSR contains the Thumb state bit, and the execution state bits for either the If-Then (IT) instruction or the Interruptible-Continuable Instruction (ICI) field for an interrupted load multiple or store multiple instruction.

## Slide 26: Cortex-M4 registers
Exception mask registers
  1-bit PRIMASK
          If set to one, will block all the interrupts apart from non-maskable interrupt (NMI) and the hard fault exception
  1-bit FAULTMASK
          If set to one, will block all the interrupts apart from NMI
  1-bit BASEPRI
          IF set to one, will block all interrupts of the same or lower level (only allowing for interrupts with higher priorities)
CONTROL: special register
  1-bit stack definition
          Set to one to use the process stack pointer (PSP)
          Clear to zero to use the main stack pointer (MSP)
Notes: The exception mask registers disable the handling of exceptions by the processor. Disable exceptions where they might impact on timing critical tasks.
The CONTROL register controls the stack used and the privilege level for software execution when the processor is in Thread mode and, if implemented, indicates whether the FPU state is active.

## Slide 27: Cortex-M4 registers
Reserved
Reserved
BASEPRI
BASEPRI
CONTROL
bit8
bit16
bit24
bit31
Stack definition
Reserved
FAULTMASK
FAULTMASK
Reserved
PRIMASK
PRIMASK

## Slide 28: Useful resources
Architecture Reference Manual:
  http://infocenter.arm.com/help/index.jsp?topic=/com.arm.doc.ddi0403c/index.html
Cortex-M4 Technical Reference Manual:
  http://infocenter.arm.com/help/topic/com.arm.doc.ddi0439d/DDI0439D_cortex_m4_processor_r0p1_trm.pdf
Cortex-M4 Devices Generic User Guide:
  http://infocenter.arm.com/help/topic/com.arm.doc.dui0553a/DUI0553A_cortex_m4_dgug.pdf